## Slide 1
KTA
v6.0
LINUX KERNEL NETWORK OBSERVABILITY
Kernel Module: C (Netfilter hooks)
GUI Frontend: Qt6 / C++
Route Daemon: Python + GeoIP
IPC: /proc VFS (7 files)
Scope: TCP + UDP real-time
Kernel Traffic
Analyzer
Real-time TCP/UDP observability from kernel space to user dashboard
Netfilter Hooks
4-Tuple Tracking
DNS Parsing
GeoIP Routing
Anomaly Engine
Qt6 15-Tab GUI
Technical Architecture Review · 2025

## Slide 2
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Problem Statement
Why Linux network observability at kernel depth is unsolved by userspace tools
Userspace Blindspots
tcpdump/Wireshark rely on libpcap AF_PACKET socket — every packet is copied to userspace, adding per-packet overhead
Userspace tools cannot atomically attribute packets to PIDs without /proc/net/tcp polling — race conditions on fast-closing connections
No single tool provides a combined view of: 4-tuple + PID + DNS hostname + TCP state + anomaly in one record
Missing Connection Lifecycle
netstat/ss snapshot /proc/net/tcp — not event-driven; SYN→ESTABLISHED transitions are invisible between polls
No standard tool tracks TIME_WAIT→CLOSED transitions with microsecond timestamps per connection
Connection teardown metadata (RST vs FIN-ACK, half-open SYN queue depth) is not exposed by any stock utility
No Integrated Threat Context
No Linux tool simultaneously correlates: port scan pattern + originating PID + DNS query + geographic route
iptables logs dropped packets but cannot feed structured anomaly events into a live monitoring dashboard
BGP route change detection, DNS leak identification, and beaconing detection each require separate tools with no unified timeline
KTA addresses this by embedding observation directly into the Netfilter hook chain — eliminating copy overhead, PID race conditions, and tool fragmentation through a unified kernel-to-userspace architecture with structured /proc output.

## Slide 3
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Solution Overview
Three-layer system: Kernel Module → /proc VFS → Qt6 GUI + Python Route Daemon
KERNEL MODULE (C)
Registers two nf_hook_ops: NF_INET_PRE_ROUTING (ingress) and NF_INET_LOCAL_OUT (egress)
Maintains jhash2-keyed hash table of kta_conn structs; state machine: SYN→ESTABLISHED→FIN→TIME_WAIT→CLOSED
Parses DNS response payloads inline in softirq using pre-allocated per-CPU buffers
8 anomaly detectors run via deferred workqueue — outside softirq to allow more complex logic
Exposes 7 structured /proc files via seq_file API with RCU-safe concurrent access
Qt6 GUI (C++)
QTimer(1000ms) drives main-thread /proc polling; parsed data fed into QAbstractTableModel subclasses
15 tabs including: Connections, Processes, DNS, Anomalies, Bandwidth, Route Map, Firewall, Trust Score
QCustomPlot renders 60-second rolling bandwidth time series; dual-line (in/out) per connection or aggregate
Firewall commands written to /proc/kta/firewall; throttle rules to /proc/kta/throttle from GUI events
Trust grade (A–F) computed per PID using weighted anomaly + volume + DNS status scoring formula
ROUTE DAEMON (Python)
Reads /proc/kta/connections every 5s; launches TCP traceroute (Scapy) for newly seen destination IPs
Each hop enriched with MaxMind GeoLite2: ASN number, AS org name, country ISO, city, latitude, longitude
Route JSON written to /proc/kta/routes via file write; GUI reads and renders on world-map QGraphicsScene
BGP change detection: diffs per-destination ASN sequence on re-trace; flags changes as BGP_ROUTE_CHANGE anomaly
Asyncio event loop with max 5 concurrent traceroutes; rate-limited to prevent network flooding
7
/proc files
15
GUI tabs
8
anomaly types
1 Hz
poll rate
<2 μs
hook cost

## Slide 4
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
System Architecture
End-to-end flow: NIC interrupt → Netfilter hook → /proc VFS → GUI + Route Daemon
NIC / Raw Network Packets
KERNEL SPACE
Netfilter Hooks
PRE_ROUTING
LOCAL_OUT
Connection Tracker
4-tuple hash table
State machine + PID
DNS Parser
+ Anomaly Engine
(8 detectors)
/proc/kta/*
7 seq_file exports
RCU-safe reads
USERSPACE
Qt6 GUI (C++)
15 tabs · 1Hz /proc polling · Bandwidth graphs · Firewall rules · Trust scoring · World threat map
Route Daemon (Python)
TCP traceroute (Scapy) · MaxMind GeoIP enrichment · BGP hop diffing · writes enriched JSON → /proc/kta/routes
↔ /proc

## Slide 5
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Kernel Module Deep Dive
C kernel module: Netfilter registration, memory model, concurrency, and /proc exposure
Netfilter Hook Registration
Registers nf_hook_ops at NF_INET_PRE_ROUTING (priority -100, ingress) and NF_INET_LOCAL_OUT (egress) via nf_register_net_hooks()
Hook callback runs in softirq context: cannot sleep, block, or use GFP_KERNEL allocations — only GFP_ATOMIC or slab cache
Returns NF_ACCEPT for monitored packets; NF_DROP for firewall-matched connections per kernel rule table
Deregistration on rmmod via nf_unregister_net_hooks() in module_exit() — no hook stale references remain
Data Structures & Memory Model
kta_conn struct: {src_ip, src_port, dst_ip, dst_port, pid, comm[16], uid, state, bytes_in, bytes_out, ts_start, ts_last, hostname[256]}
Hash table via DEFINE_HASHTABLE(kta_table, 14): 2^14 = 16384 buckets; keyed by jhash2() of 4-tuple for O(1) average lookup
RCU protects the table: readers use rcu_read_lock()/rcu_read_unlock(); writers perform copy-modify-swap with synchronize_rcu()
Per-CPU counters via percpu_counter avoid spinlock contention on packet byte accounting in hot path
Concurrency & Workqueue
Spinlocks protect per-conn state transitions (SYN→ESTABLISHED); held for <200ns to avoid softirq stall
Anomaly scoring and DNS cache eviction deferred via queue_work(system_wq) — runs in process context, allows mutex
GC workqueue (delayed_work) fires every 30s: walks table, removes conns exceeding TIME_WAIT (120s) or idle timeout
/proc File Registration
7 files created via proc_create() with custom proc_ops structs (.proc_read via seq_file, .proc_write where needed)
seq_file API: start/next/stop iterator prevents buffer overflow on large connection tables (>1000 entries)
Write-capable files (/proc/kta/firewall, /proc/kta/config) accept commands from GUI — processed in proc_write handler in process context

## Slide 6
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Connection Tracking Mechanism
TCP 4-tuple hash table + state machine: allocation, transition, expiry, GC
4-Tuple Tracking Logic
Lookup key: jhash2({src_ip, src_port, dst_ip, dst_port}) — reverse 4-tuple also checked (reply packets hit same conn record)
On SYN: allocate kta_conn from dedicated kmem_cache (slab); insert into hash table under spinlock; capture PID via current->pid
On SYN-ACK: transition state ENUM to SYN_RECV; record RTT estimate from ktime_get() delta since SYN timestamp
On ACK completing 3-way handshake: state → ESTABLISHED; socket-to-task mapping validated via sock_task_pid()
On FIN: state → FIN_WAIT (client) or CLOSE_WAIT (server); retained for TIME_WAIT window (2×MSL = 120s)
On RST: immediate transition to CLOSED; conn marked for GC on next 30s workqueue pass without TIME_WAIT delay
TCP State Machine (KTA)
CLOSED
SYN_SENT
SYN_RECV
ESTABLISHED
FIN_WAIT
CLOSE_WAIT
TIME_WAIT
CLOSED
SYN
SYN+ACK
ACK
FIN
FIN
2×MSL

## Slide 7
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Process Attribution + Resolver
Mapping network packets back to Linux processes: PID, TGID, comm, UID, cmdline
Kernel-Side PID Capture
PID captured at SYN time via current->pid in NF_INET_LOCAL_OUT hook — runs in originating task context, no race possible
Server-side connections (PRE_ROUTING): PID resolved by walking inet_hashinfo socket table to match 4-tuple to owning socket struct
comm[] (16-byte task name) and uid (task->cred->uid) captured atomically with PID at SYN packet time
TGID stored alongside PID to roll up threads to their parent process in GUI process aggregation view
Userspace Enrichment (Qt6 GUI)
GUI reads /proc/<pid>/cmdline (full command line) and /proc/<pid>/exe (symlink to binary) at display time
Parent PID (PPID) resolved from /proc/<pid>/status for process tree view — identifies service ancestry
Per-PID bandwidth aggregation: GUI sums bytes_in/bytes_out across all conns sharing the same PID
Process death handled: PID stored in kta_conn even after task_struct freed — GUI shows [exited:PID] with last-known comm
Edge Cases & Container Support
Race: process exits before hook fires — PID captured as-is in kta_conn; /proc/<pid> read may fail, GUI falls back to stored comm[]
Kernel threads (kworker, ksoftirqd): identified by PID in kthread range or empty cmdline; tagged as [kernel] in display
Container namespaces: task_pid_vnr() returns container-local PID; host PID stored separately via task_pid_nr() for cross-namespace visibility
UDP attribution: connectionless — PID captured at sendmsg() hook (LOCAL_OUT) per datagram; server-side attribution not available for stateless UDP servers
Multi-process listeners (e.g. nginx workers): each accept() creates conn attributed to accepting worker PID; PPID links all to master process

## Slide 8
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
DNS Parsing + Mapping
Kernel-level DNS interception: response parsing, IP→hostname cache, leak detection
Kernel DNS Interception
Intercept point: NF_INET_PRE_ROUTING; filter: UDP with src_port == 53 (DNS response direction)
skb_header_pointer() safely reads DNS payload without linearizing skb — avoids unnecessary data copy
DNS header parsed: checks QDCOUNT, ANCOUNT; walks answer section for type A (IPv4) and AAAA (IPv6) records
Label pointer decompression (0xC0 prefix) handled iteratively with hop limit to prevent infinite-loop attack on malformed packets
IP→Hostname Cache
Resolved pairs stored in kta_dns_cache hash table (2^12 buckets) with per-entry 60-second TTL from DNS response TTL field
On new connection: dst_ip looked up in cache; match written to kta_conn.hostname[256] — GUI displays name without re-resolving
Cache exported via /proc/kta/dns: ip_addr, hostname, ttl_remaining, query_count per entry using seq_file
Eviction: LRU with 4096-entry hard cap; oldest entry freed on overflow via linked-list LRU tracking — bounds kernel heap usage
DNS Leak Detection
Leak condition: DNS query (UDP dst_port 53) egresses via interface whose ifindex ≠ configured tunnel_ifindex kernel parameter
Detected leaks create DNS_LEAK anomaly record: {ts, src_ip, dst_ip, query_name, iface_name, severity=HIGH}
Split-horizon DNS exclusion: queries to RFC1918 dst_ip ranges on non-tunnel iface are not flagged as leaks
tunnel_ifindex configurable via /proc/kta/config key=value write — runtime-reconfigurable without rmmod
Parsing Safety Constraints
All DNS parsing runs in softirq: no GFP_KERNEL, no sleeping — uses pre-allocated per-CPU 512-byte parse buffers (alloc_percpu at init)
Bounds checks on every field offset: truncated/malformed packets detected and silently skipped to prevent kernel panic
DNS payload capped at 512 bytes (UDP) / 64 KB (TCP); buffer overflow impossible via strict offset validation before any read
Parsing stats exported in /proc/kta/stats: dns_parsed, dns_malformed, dns_cache_hits, dns_cache_misses

## Slide 9
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Route Tracing System
Python daemon: TCP traceroute + MaxMind GeoIP enrichment + BGP change detection
TCP Traceroute Mechanism
Uses Scapy to send TCP SYN probes with TTL 1→30 to destination — avoids ICMP-blocking firewalls that drop UDP probes
Per-hop response: ICMP TTL Exceeded (transit router) or TCP RST/SYN-ACK (final destination) — RTT measured via ktime
Timeout per hop: 2 seconds with 3 retries; non-responding hops marked as '*' and excluded from ASN comparison
Traceroute triggered only on first-seen destination IP — cached results used for known destinations to avoid redundant probing
GeoIP Enrichment (MaxMind)
Each responding hop IP resolved via geoip2 Python library against GeoLite2-ASN.mmdb and GeoLite2-City.mmdb
Fields per hop: {hop_n, ip, asn, org, country_iso, city, latitude, longitude, rtt_ms}
Enriched route serialized as JSON array, written to /proc/kta/routes via open()+write() — kernel proc_write stores in per-dst slot
GUI reads /proc/kta/routes and renders hops as nodes on QGraphicsScene world map with latency-weighted edge thickness
BGP Change Detection
Daemon maintains previous_routes dict: {dst_ip: [asn_per_hop]}; on re-trace (every 60s for active dests), diffs ASN sequences
Any ASN change at any hop position creates BGP_ROUTE_CHANGE anomaly with {dst_ip, hop_n, old_asn, new_asn, timestamp}
Useful for detecting BGP prefix hijacks where traffic is silently redirected through a foreign AS mid-session
Diff logic ignores '*' hops to suppress false positives from transient ICMP filtering at transit routers
Daemon Architecture
Single asyncio event loop; per-destination traceroute runs as asyncio subprocess (Scapy in child process for isolation)
Concurrency cap: semaphore limits to 5 simultaneous traceroutes — prevents network flooding on high-connection hosts
IPC exclusively via /proc — no sockets, no shared memory, no Unix pipes; simplifies privilege model (daemon needs raw socket)
Restart-safe: daemon re-reads /proc/kta/connections on startup and rebuilds route cache for all active destination IPs

## Slide 10
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Anomaly Detection Engine
8 kernel/daemon detectors with tunable thresholds — deferred workqueue execution
Port Scan
SYN to ≥15 distinct dst_ports from same src_ip in 10s sliding window. Tracked per-source via circular buffer of (timestamp, dst_port) tuples. Threshold configurable via /proc/kta/config.
SYN Flood
SYN-without-ACK rate from a single src_ip exceeds 50 pkt/s. Per-src atomic counter decremented by 1Hz hrtimer; threshold exceeded triggers anomaly record with src_ip and rate.
Burst Traffic
Single connection byte delta exceeds 100 MB/500ms threshold. Measured per-conn in 500ms workqueue tick via bytes_in/out delta. Threshold tunable in /proc/kta/config.
DNS Leak
DNS query egresses via non-tunnel interface when VPN is active. Detected by comparing packet ifindex against tunnel_ifindex kernel parameter at NF_INET_LOCAL_OUT hook time.
BGP Route Change
Route daemon detects ASN change on any traceroute hop. Written as anomaly to /proc/kta/anomalies from Python via proc_write; runs in process context, safe for full JSON write.
Long-Lived Connection
TCP connection active beyond 24h with no traffic — possible persistent C2 beaconing channel. Checked during 30s GC workqueue pass via ktime_get() delta against ts_last_data.
Unknown DNS
Connection dst_ip has no matching DNS cache entry — direct-IP connection bypassing DNS resolution. Flagged as potential data exfiltration or malware C2 on external addresses.
High Entropy Port
dst_port > 49151 (OS ephemeral range) with no known service match for external connections originating from server processes (UID < 1000). Scored as suspicious in trust engine.

## Slide 11
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
/proc Interface Design
7 structured VFS files: schema, access mode, format, consumer, and concurrency model
File
Mode
Format
Content & Purpose
Consumer
/proc/kta/connections
R
TSV
src/dst IP:port, PID, comm, state, bytes_in/out, hostname, ts_start, ts_last
GUI + Daemon
/proc/kta/anomalies
R
JSON
type, src_ip, dst_ip, pid, ts, severity, detail — ring buffer of last 1024 events
GUI
/proc/kta/dns
R
TSV
ip_addr, hostname, ttl_remaining, query_count — IP→hostname cache snapshot
GUI
/proc/kta/routes
R/W
JSON
dst_ip → [{hop, ip, asn, org, lat, lon, rtt}] — written by daemon, read by GUI
GUI(R) Daemon(W)
/proc/kta/stats
R
Plain
total_conns, active, dns_hits, anomaly_count, hash_collisions, mem_kb
GUI
/proc/kta/firewall
W
CMD
Text cmds: DROP <ip>, ALLOW <ip>, THROTTLE <ip> <kbps>, EXPIRE <ip> <ttl_s>
GUI
/proc/kta/config
R/W
KEY=VAL
Tunable thresholds: scan_window, syn_rate, idle_timeout, burst_mb, tunnel_ifindex
GUI
Concurrency model: All /proc read handlers use rcu_read_lock() — zero blocking of the kernel hook path. seq_file handles multi-page output via start/next/stop iterator preventing partial reads. Write handlers (firewall, config) use mutex_lock() — safe because writes occur infrequently from GUI user actions. /proc/kta/routes write from daemon uses copy_from_user() + bounded JSON parse (max 64 KB) inside proc_write running in process context — allows kmalloc(GFP_KERNEL) safely.

## Slide 12
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Qt6 GUI — Architecture & Tab Overview
C++ Qt6 application: polling model, data binding, rendering pipeline, and 15 functional tabs
Qt6 Architecture
Main thread only: QTimer(1000ms) triggers /proc reads via QFile::readAll() — VFS read is atomic at seq_file level
Parsed records loaded into QAbstractTableModel subclasses; QTableView updates via dataChanged() signal — no full repaint
QSortFilterProxyModel enables O(log n) multi-column sort on 10k+ connection rows without UI stall during sort
QCustomPlot renders dual-line bandwidth time series (in/out); 60-point ring buffer = 60-second rolling window at 1Hz
Firewall/throttle commands: GUI writes plaintext command to /proc/kta/firewall via QFile::write() on user button click
15 Tabs
Connections
Processes
DNS Map
Anomalies
Bandwidth
Route Map
Firewall
Trust Score
Cost Tracker
Threat Map
BGP Monitor
DNS Leak
Throttle
Packet Log
Settings
Rendering & Performance
Anomaly rows highlighted via QStyledItemDelegate: severity-mapped colors (red/amber/blue) without model repaint
Route Map tab: QGraphicsScene with hop nodes and latency-weighted edges overlaid on embedded SVG world map
Memory: each Qt connection record ~256 bytes; 10k connections = 2.5 MB in model — well within acceptable bound
Chart updates: only dirty data points re-rendered; QCPGraph::setData() with preserveSortedData=false for speed
Key UI Features
Trust Score tab: letter grade A–F per PID with trend arrow; computed from weighted anomaly + volume + DNS status formula
Cost Tracker: bytes-per-interface × $/GB configurable rate; aggregated per process and per destination ASN per billing period
Threat Map: external destination IPs plotted on world map using GeoIP lat/lon data from route daemon JSON
BGP Monitor: timeline view of ASN changes per destination with old_asn/new_asn diff and hop position highlighted

## Slide 13
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Advanced Features
Firewall control, trust scoring, bandwidth throttling, and cloud cost tracking
Firewall & Packet Filtering
GUI writes DROP/ALLOW/THROTTLE commands to /proc/kta/firewall; kernel proc_write parses and updates in-kernel rule list
Rules stored as {src_ip, dst_ip, dst_port, action, expire_ts} structs in a singly-linked kernel list protected by spinlock
NF_DROP returned from Netfilter hook for packets matching active DROP rules — no packet copy to userspace occurs
Timed rules: expire_ts set by GUI (e.g. block for 60s); GC workqueue removes expired rules every 30s via ktime_get() comparison
Trust Scoring System (A–F)
Score computed per PID each polling cycle: base 100 minus weighted penalties from anomaly records attributed to that PID
Penalty weights: SYN flood –30, port scan –25, DNS leak –20, BGP route change –15, unknown DNS –10, long-lived conn –5
Grade bands: A=90–100, B=75–89, C=60–74, D=45–59, F=<45; trend arrow shows score delta over last 5 cycles
Score resets to 100 when PID exits and a new process takes the same PID — no historical penalty inheritance
Bandwidth Throttling
Token bucket algorithm in kernel: N bytes replenished per 100ms hrtimer; excess packets above bucket depth returned NF_DROP
THROTTLE command format: THROTTLE <src_ip> <dst_ip> <kbps>; stored in kernel throttle_table indexed by 4-tuple prefix
Throttle state exported in /proc/kta/stats: per-rule current_rate_kbps, bucket_level_bytes, drop_count for GUI display
Cost Tracking
Per-connection bytes aggregated per interface (eth0, wlan0, tun0); user-configured $/GB rate applied per interface in GUI
Cost formula: (bytes_total / 1e9) × rate_per_gb; displayed per PID and per destination ASN in Cost Tracker tab
Configurable billing period (hourly/daily/monthly) with rolling cost accumulation since KTA module load time
Designed for cloud VM egress attribution: identifies which process generates most billable outbound data volume

## Slide 14
KTA v6.0 — Kernel Traffic Analyzer | Technical Architecture Review
© 2025
Performance + Design Constraints
Kernel engineering tradeoffs: softirq limits, memory bounds, latency budget, async delegation
Softirq Context Constraints
Netfilter hook runs in softirq: must not sleep, block on mutex, call vmalloc/GFP_KERNEL, or dereference user memory
All hot-path allocations use kmem_cache (slab) pre-allocated at module_init(); GFP_ATOMIC reserved for rare dynamic cases
DNS parsing uses pre-allocated per-CPU 512B buffers (alloc_percpu at init) — zero runtime allocation in softirq path
Complex operations (anomaly scoring, cache eviction, GC) deferred to workqueue via queue_work() — process context, no restrictions
Memory Model & Footprint
Connection hash table: 2^14 buckets × 8B pointer = 128 KB static; each kta_conn ≈ 320 bytes → 10k conns = 3.2 MB total
DNS cache: max 4096 entries × ~128 bytes = 512 KB; LRU eviction bounds heap usage at this fixed ceiling
Total module kernel memory at 10k connections: ~4 MB — acceptable on any 64-bit host with 1+ GB RAM
vmalloc used only for large temporary seq_file buffers; freed immediately after /proc read completion
Latency & Throughput
Per-packet hook overhead: <2 μs on Intel i7-class CPU (hash lookup + counter update + state check via benchmark)
Practical throughput limit: 1 Gbps sustained with <5% CPU overhead — tested via iperf3 on 4-core VM
At 10 Gbps line rate (~14 Mpps for 64B pkts), 2 μs/pkt budget is exceeded; KTA targets monitoring, not line-rate filtering
RCU read-side critical section: ~50 ns average — negligible vs packet processing time in any practical scenario
Async Workqueue Design
system_wq handles short bounded items (anomaly check, score update); system_long_wq for GC to avoid occupying shared wq
Workqueue items access connection table via rcu_read_lock() — fully concurrent with Netfilter hook path
delayed_work for GC every 30s: expires TIME_WAIT conns, evicts stale DNS entries, cleans expired firewall rules
/proc write handlers (from GUI/daemon) run in process context — safe for mutex_lock(), kmalloc(GFP_KERNEL), copy_from_user()

## Slide 15
KTA
v6.0
Conclusion & Impact
7
/proc interfaces
15
GUI tabs
8
anomaly detectors
<2 μs
hook overhead
1 Gbps
tested throughput
What KTA Demonstrates
Kernel-Depth Observability Without Copy Overhead
Proves that production-grade network monitoring is achievable entirely within Netfilter hooks, eliminating the PID race conditions and per-packet copy overhead inherent in all libpcap-based tools.
Zero-Copy /proc IPC Architecture
The /proc VFS interface pattern — RCU-safe reads, seq_file multi-record output, proc_write command channel — provides stable, low-overhead IPC between kernel and userspace with no socket complexity.
Unified Multi-Layer Correlation
Simultaneous correlation of PID → connection → DNS hostname → geographic route → anomaly in a single UI is not achievable with any combination of existing Linux monitoring tools.
Threat-Aware Host Observability
8 anomaly detectors, trust scoring, and BGP monitoring make KTA actionable as a lightweight host-based IDS — beyond passive observation, enabling real-time policy enforcement via kernel firewall integration.